OVERVIEW

Simplicity

- Familiar "Analog-like" control

- Intuitive multi-layer layout

- Moving Faders, "1-step" functionality, dedicated knobs, faders and buttons

- Auto Display Change/Auto Channel Select

- Multi-LED's, backlit LCD, Peak/Presence Indicators

- CUT, COPY, PASTE and UNDO editing

Control

- Moving fader dynamic and scene automation with instantaneous recall

- 38 Total Inputs, 6 AUX Sends, 6 AUX Returns with 2-band parametric EQ

- 8 buses (sub-groups) that can be digitally routed using a built-in patchbay for a total of 24 digital and analog I/O's

- Complete digital format compatibility and exchangeability

48 true 4-band parametric equalizers on every channel, bus and L/R masters

- High/low band selectable peaking/shelving or high-pass/low-pass filter

- Extremely narrow (0.1 octave) or wide (10 octave) Q parameters

- + or – 15dB boost or cut in 1/2 dB steps

42 full function Compressor/Gate/Limiter or Expanders

- Delays up to 300 ms on every channel

- Discrete outputs with 5.1 panning for surround sound capability

- Custom/MIDI Layer, MIDI Machine Control (MMC) and PC ports for Mac/Win software

- 21-100mm Motorized Faders, Jog-Dial, Cursor keys and 10 key Keypad

- Optional Tandem operation doubles the number of inputs to 76 total

Sound

- 16-high quality ultra low noise padless mic pre-amps

- 32-bit Internal signal processing (192dB Dynamic range)

- 24-bit 7th order delta sigma modulation 64 times over-sampling A/D converters on inputs

- 24-bit 64 times over-sampling D/A converters on Master and Monitor A outputs

- Separate power supply units (internal) for analog and digital circuits

- Custom LSI for high speed DSP signal processing

- Linear response, low noise, low THD, equalizer, compressor and expander characteristics

- Built in dithering for recording to 23-16-bit devices.

- Powerful Headphone amp

Connectivity

- 16 balanced XLR and 1/4" TRS Mic/line analog inputs

- 16 analog inserts (pre A/D)

- AES/S/PDIF (2 Ch.) digital I/O, Word Clock In/Out, MIDI, IN/OUT, MIDI Machine Control (MMC) RS-422/485, are standard

- Optional ADAT lightpipe, TASCAM/TDIF, AES-EBU-SPDIF and analog AD-DA 8-Channel

- SMPTE/Video-sync

Expandability

- Tandem (dual-console) operation

- SMPTE/V-Sync, AES/EBU-SPDIF, TDIF, ADAT, Analog (8 Ch.) Audio I/O cards

- High resolution Meter Bridge and " MAX" Automation Expansion software