Specifications:

It features a built-in slot for a flash memory card or MemoryStick for still image storage. Up to 988 JPEG pictures can be stored in one 64 MB MemoryStick. The stored images can be mixed or keyed to the live image allowing logo insertion and/or mix effects. The built-in electronic zoom lens features Autofocus and SuperSteadyShot with a high MTF 12X high MTF quality optical lens with manual Zoom, Focus and Iris control.

A high resolution (500 lines) B&W viewfinder and a color swing out bright color LCD panel are included to make shooting a breeze. A software package for logo generation and included USB port adapter are standard.

# Features

- High quality digital component video and audio recording using DVCAMO format.

- High quality digital component video and audio recording using DVO format (SP mode)

- Newly developed three 380K pixels 1/3" CCDs

- SuperSteadyShotOand Autofocus

- 12X optical zoom, 20/48X digital zoom

- 530 TV lines of horizontal resolution

- 2 lux minimum illumination

- Auto or manual exposure

- Built in speaker

- 480p VGA quality 640x480 progressive scan still image capturing

- Tape photo mode for recording still images to tape

- Memory still mode. Up to 988 images can be recorded on the optional 64 MB flash memory

- USB flash memory port for PC included

- 4 MB MemoryStickO included allows up to 60 JPEG images

- Directional shotgun (mono) microphone included

- Two independent XLR audio inputs with independent audio level control, line/mic select and phantom power are provided

- 16:9/4:3 aspect ratio switchable. 4:3 native.

- 16 bit/12 bit PCM audio for two or four channel audio modes

- Audio dubbing capabilty

- i.Link (IEEE1394 compliant) input and output built in interface

- Analog input using the S-Video connector

- S-Video Input to DV i.Link output A/D conversion capability

- High 500 lines H. resolution professional B&W viewfinder

- Color 2.5" swing out reversible 200,000 dot LCD panel display

- Digital video effects.

  - Fader

  - Flash Motion

  - Trail

  - Old Movie (Sepia and shutter effects)

  - Luminance Key

- 3 Fader modes: black, monotone, overlap to last image from still

- Electronic title function

- Chroma- key for title, image or logo insertion from the memory stick

- Variable shutter speeds

- Digital program editing using i.LINK . Up to 20 programs can be preset for auto edit

- Custom AE ( auto exposure) mode

- Time code with preset and user bits capability

- 70% and 100% Zebra indicator for perfect exposure

- Spotlight and backlight buttons for accurate exposure in difficult shots

- Guide frame for image alignment

- Long recording capability. Up to 8 hours with one NP-F960 battery (not included)

- Time / Date stamp with seconds readout (recorded on video) for legal or identification

- Software for Logo generation included: Picture Gear 4.1 Lite

- Manual functions for the demanding professional:

  - Shutter speeds

  - Independent Audio recording levels

  - White balance

  - AE shift

  - Iris

  - Zoom

  - Focus