Video

Routing 					84 Series: 8 x 4 matrix

88 Series: 8 x 8 matrix

124 Series: 12 x 4 matrix

128 Series: 12 x 8 matrix

168 Series: 16 x 8 matrix

1616 Series: 16 x 16 matrix

2412 Series: 24 x 12 matrix

2424 Series: 24 x 24 matrix

3216 Series: 32 x 16 matrix

3232 Series: 32 x 32 matrix

Gain 						Unity

Bandwidth 					425 MHz (-3dB), fully loaded

84/88/124/128/168/1616 Series 	0 - 10 MHz: no more than +0.1dB to -0.1dB

0 - 130 MHz: no more than +6dB to -0.8dB

2412/2424/3216/3232 Series 	0 - 10 MHz: no more than +0.1dB to -0.1dB

0 - 130 MHz: no more than +4dB to -0.1dB

# Crosstalk

84/88/124/128/168/1616 Series

-80dB @ 1 MHz, -65dB @ 10 MHz, -55dB @ 30 MHz, -42dB@ 100 MHz

2412/2424/3216/3232 Series

-55dB @ 10 MHz, -45dB @ 30 MHz, -37dB @ 100 MHz

Switching speed 				200 ns (max.)

Video input

Number/signal type 	8, 12, 16, 24, or 32 RGBHV, RGBS, RGsB, RsGsBs, HDTV, component video, S-video, composite video

Connectors 					84/88 Series: 8 x 5 BNC female

124/128 Series: 12 x 5 BNC female

168/1616 Series: 16 x 5 BNC female

2412/2424 Series: 24 x 5 BNC female

3216/3232 Series: 32 x 5 BNC female

Nominal level 	1V p-p for Y of component video and S-video, and for composite video

0.7V p-p for RGB

0.3V p-p for R-Y and B-Y of component video, and for C of S-video

Minimum/maximum levels 		Analog: 0.5V to 2.0V p-p with no offset

Impedance 					75 ohms

Return loss 					-30dB @ 5 MHz

Maximum DC offset 			1.5V

Video output

Number/signal type 	4, 8, 12, 16, 24, or 32 RGBHV, RGBS, RGsB, RsGsBs, HDTV, component video, S-video, composite video

Connectors 					84/124 Series: 4 x 5 BNC female

88/128 Series: 8 x 5 BNC female

168 Series: 8 x 5 BNC female

1616 Series: 16 x 5 BNC female

2412 Series: 12 x 5 BNC female

2424 Series: 24 x 5 BNC female

3216 Series: 16 x 5 BNC female

3232 Series: 32 x 5 BNC female

Nominal level 	1V p-p for Y of component video and S-video, and for composite video

0.7V p-p for RGB

0.3V p-p for R-Y and B-Y of component video, and for C of S-video

Minimum/maximum level 		2V p-p

Impedance 					75 ohms

Return loss 					-30dB @ 5 MHz

DC offset 					±5mV maximum: with input at 0 offset

Switching type 				Triple-Action™

Sync

Input type 					RGBHV, RGBS, RGsB, RsGsBs

Output type 					RGBHV, RGBS, RGsB, RsGsBs

Input level 					0.5V to 5.0V p-p,: 4.0V p-p normal

Output level 				AGC to TTL: 4V to 5V p-p, unterminated

# Input impedance

84/88/124/128 Series 		Inputs 1 to 4: 75 or 510 ohms, switchable

Inputs 5 to 12: 510 ohms

168/1616 Series 			Inputs 1, 3, 5, 7: 75 or 510 ohms, switchable

Inputs 2, 4, 6, 8, and 9 to 16: 510 ohms

2412/2424/3216/3232 Series 	Inputs 1 to 8: 75 or 510 ohms, switchable

Inputs 9 to 32: 510 ohms

Output impedance 			75 ohms

Polarity 					Positive or negative (follows input)

Audio — audio models only

Routing 					84 Series: 8 x 4 stereo matrix

88 Series: 8 x 8 stereo matrix

124 Series: 12 x 4 stereo matrix

128 Series: 12 x 8 stereo matrix

168 Series: 16 x 8 stereo matrix

1616 Series: 16 x 16 stereo matrix

2412 Series: 24 x 12 stereo matrix

2424 Series: 24 x 24 stereo matrix

3216 Series: 32 x 16 stereo matrix

3232 Series: 32 x 32 stereo matrix

# Gain

8-, 12-, 16-input models 		Unbalanced output: 0dB; balanced output: +6dB

24- and 	32-input models: Unbalanced output: -6dB; balanced output: 0dB

Frequency response 			20 Hz to 20 kHz, ±0.05dB

THD + Noise 				0.03% @ 1 kHz at rated nominal level

S/N 						>90dB, balanced, at rated maximum output (21dBu)

Crosstalk 					<-80dB @ 1 kHz, fully loaded

Stereo channel separation 		>80dB @ 1 kHz

CMRR 					>75dB @: 20 Hz to 20 kHz

Audio input — audio models only

Number/signal type 			8, 12, 16, 24, or 32 stereo, balanced/unbalanced

Connectors 	(8, 12, 16, 24, or 32) 3.5 mm captive screw connectors, 5 pole

Impedance 					>10 kohm, balanced/unbalanced, DC coupled

Nominal level 				-10dBV (316mV)

Maximum level 				+19.5dBu, (balanced or unbalanced) at 1%THD+N

# Input gain adjustment

84/88/124/128/168/1616 Series 	-15dB to +9dB, adjustable per input by RS-232/422 or front panel

2412/2424/3216/3232 Series 	-18dB to +24dB, adjustable per input by RS-232/422 or front panel

Audio output — audio models only

Number/signal type 	4, 8, 12, 16, 24, or 32: stereo, balanced/unbalanced

Connectors 	(4, 8, 12, 16, 24, or 32) 3.5 mm captive screw connectors, 5 pole

Impedance 					50 ohms unbalanced, 100 ohms balanced

Gain error 					±0.1dB channel to channel

Maximum level (Hi-Z) 			>+21dBu, balanced or unbalanced at 1%THD+N

Maximum level (600 ohm) 		>+15dBm, balanced or unbalanced at 1%THD+N

Control/remote — switcher

Serial control port 				1 RS-232 or RS-422, 9-pin female D connector

Baud rate and protocol 			9600, 8-bit, 1 stop bit, no parity

Serial control pin configurations 	2 = TX, 3 = RX, 5 = GND

Ethernet control port 	2412/2424/3216/3232 Series only: 1 RJ-45 female connector

Ethernet data rate 	2412/2424/3216/3232 Series only: 10/100Base-T, half/full duplex with autodetect

Ethernet protocol 	2412/2424/3216/3232 Series only: ARP, ICMP (ping), TCP/IP, Telnet, HTTP

## Program control

2412/2424/3216/3232 Series 	Extron's control program for Windows®

Extron's Simple Instruction Set™ _ SIS™

Microsoft Explorer, Netscape Navigator, Telnet

All other models 			Extron's control program for Windows®

Extron's Simple Instruction Set™ _ SIS™

General

## Power

8-, 12-, 16-input models 	100VAC to 240VAC, 50/60 Hz, internal, autoswitchable

84/88/124/128 			30 watts

168/1616 				36 watts

24- and 32-input models 	2 (primary and redundant), 100VAC to 240VAC, 50/60 Hz, internal, autoswitchable

2412/2424 Series: 150 watts

3216/3232 Series: 180 watts

Temperature/humidity 	Storage -40° to +158°F (-40° to +70°C) / 10% to 90%, non-condensing

Operating +32° to +104°F (0° to +40°C) / 10% to 90%, non-condensing

Rack mount 				Yes, with included parts

Enclosure type 				Metal

## Enclosure dimensions

84/88/124/128 Series 		5.25" H x 17.0" W x 9.4" D: (3U high, full rack width)

13.3 cm H x 43.2 cm W x 23.9 cm D

(Depth excludes connectors.: Width excludes rack ears.)

168/1616 Series 			10.5" H x 17.0" W x 9.7" D: (6U high, full rack width)

26.7 cm H x 43.2 cm W x 24.6 cm D

(Depth excludes connectors.: Width excludes rack ears.)

2412/3216 HV and HVA Series 	14.0" H x 17.0" W x 12.0" D: (8U high, full rack width)

(35.5 cm H x 43.2 cm W x 30.5 cm D)

(Depth excludes connectors.: Width excludes rack ears.)

2424/3232 HV and HVA Series 	17.5" H x 17.0" W x 12.0" D: (10U high, full rack width)

(44.5 cm H x 43.2 cm W x 30.5 cm D)

(Depth excludes connectors.: Width excludes rack ears.)

## Product weight

84/88/124/128 Series 		14.4 lbs (6.5 kg)

168/1616 Series 			19.4 lbs (8.8 kg)

2412/3216 Series 			32 lbs (14.5 kg)

2424/3232 Series 			36 lbs (14.5 kg)

## Shipping weight

84/88/124/128 Series 		21 lbs: (9.5 kg)

DIM weight: 25

168/1616 Series 			26 lbs (11.8 kg)

DIM weight: 34

2412/3216 Series 			35 lbs (15.9 kg)

DIM weight: 77

2424/3232 Series 			40 lbs (18.1 kg)

DIM weight: 77

Vibration 	ISTA/NSTA 1A in carton (International Safe Transit Association)

Listings 					UL, CUL

## Compliances

2412/2424/3216/3232 Series 	CE, FCC Class A, VCCI, AS/NZS, ICES

All other models 			CE, FCC Class A

MTBF 						30,000 hours

Warranty 					3 years parts and labor