### Sound Domes

# DOUBLE

Isolation				12dB

Stereo Separation		 	8dB

## Listening Region Dimensions		30”H x 28”W x 12”D (0.8m x 0.7m x 0.3m)

## Physical Properties

Diameter:	32” (.8m)

Height:		16” (.4m)

Weight:	17lbs. (8.2kg)

Installation options	A, B, C (see below)

Mounting Height Options (see below)

## Installation Options

- Three-Point Cable (hardware included)

- Single-threaded rod (additional hardware required)

- TriMount pole system (optional

## Mounting Height Options

Measurements are from the floor to the bottom edge of the dome.

For Sitting Listener:	6.5* or 7.5 feet (2 or 2.3m)

For Standing Listener:		7.5*, 8, or 9 feet (2.3, 2.4, 2.7m)

*Recommended mounting height

## Amplifier Power Requirements

Minimum:	1 watts per Channel

Maximum:	50 watts per Channel

## Speaker Impedance	6 Ohms

Sensitivity	102dB SPL 1 watt, 1 meter @1kHz

Frequency Response	150Hz – 20kHz, +/-2dB*

*When using Localizer Virtuoso amplifier only

Specifications using an alternative amplifier will differ